## Slide 1: CEMENT TEST
BY
MOHD ZAKER
ASST PROFESSOR

## Slide 2: Welcome to Civil Engineering

## Slide 3: Introduction
In general, cement is described as material used to bind the mineral fragments called aggregates
The cement paste acts as glue which makes a cohesive mass with all the aggregates
This bonding is important as the concrete fails not because of less strength of aggregates but mainly due to failure of bonding

## Slide 4: Test Of Cement;
Normally two types of cement tests are conducted
Laboratory test of cement
Field test of Cement

## Slide 5: Laboratory test of cement
For examining the suitability of cement in the laboratory, the following tests are performed
Fineness test
Consistency test
Specific gravity
Initial and Final setting time test
Soundness test
Compressive strength test
Loss of Ignition Test

## Slide 6: FINENESS TEST
Laboratory test of cement
Fineness of cement affects hydration rate hence the rate of strength gain. The smaller the particle size, the greater the surface area-to-volume ratio, and thus, the more area available for water-cement interaction per unit volume. Therefore finer cement reacts faster with water and the rate of development of strength and corresponding heat of hydration is high.
Fineness test is used to check the proper grinding of cement and measures the surface area of the cement particles per unit mass.

## Slide 7: Laboratory test of cement
There are two method of testing fineness of cement;
 Sieving method
 Air permeability method (Blaine)
Sieving method
In this method dry sieving is used, the principle of this is that we
determine the proportion of cement whose grain size is larger
then specified sieve size.
The apparatus used;
 90µm IS Sieve
 Balance capable of weighing 10g to the nearest 10mg
 A nylon or pure bristle brush, preferably with 25 to 40mm -for cleaning the sieve.

## Slide 8: Procedures;
Laboratory test of cement
Weigh approximately 10g of cement to the nearest 0.01g and place it on the sieve
Agitate the sieve by swirling, planetary and linear movements, until no more fine material passes through it.
Weigh the residue and express its mass as a percentage of the quantity first placed on the sieve to the nearest 0.1 percent.
Note: The weight of residue should not exceed 10% for Ordnally Portland Cement
(OPC).
Disadvantages of finenes cement
 Higher fineness requires higher grinding resulting in high cost
 Finer cements deteriorate faster upon exposure to atmosphere.
 Finer cements require more gypsum for proper hydration. ( unsoundness of
cement)
 Finer cements require more water hence high pores.

## Slide 9: Laboratory test of cement
Air permeability method (Blaine)
The aim is to determine the fineness or surface area per gram of the cement.
Procedures;
 Put a filter paper into the cell then weight 2.84g of cement sample into it.
 Put another filter paper on it and compress with the plunger.
 Attach the cell on top of the U-tube manometer.
 Evacuate the air in the manometer through the side tube using the aspirator bulb
until the oil reaches level 1.
 Close the side valve and monitor the oil as it start to fall.
 Using a stop watch, measure the time taken for the oil to fall from level 2 to level 3
Blaine =k√t where k is 523.0547
Example: when t is obtained a 29sec
S=523.0547√29
S=2817cm2/gm
Laboratory test of cement

## Slide 10: CONSISTENCY TEST
Laboratory test of cement
What is consistency?
Consistency refers to the relative mobility of a freshly mixed cement paste or mortar or its ability to flow. The test aim to measure the quantity of water required to produce a cement paste of standard or normal consistency
Apparatus
 Vicat apparatus
 Balance, whose permissible variation at a load of 1000g should
be +1.0g,
 Gauging trowel

## Slide 11: Laboratory test of cement
Procedures;
(i) Weigh approximately 400g of cement and mix it with a weighed
quantity of water. Note: The time of gauging should be between 3
to 5 minutes.
Fill the Vicat mould with paste and level it with a trowel.
Lower the plunger gently till it touches the cement surface.
Release the plunger allowing it to sink into the paste.
It is defined as that percentage of water added to form the paste which allows a penetration of 10  1 mm of the Vicat plunger. The principle also is that standard consistency of cement at which the Vicat plunger penetrates to a point 5-7mm from the bottom of Vicat mould.

## Slide 12: SPECIFIC GRAVITY TEST
Laboratory test of cement
To determine the specific gravity is normally defined as the ratio between the weight of a given volume of material and weight of an equal volume of water. To determine the specific gravity of cement, kerosene which does not recent with cement is used.
The mass of a unit volume of the solids or particles, excluding air between particles. The particle density o3f Portland cement ran3ges from 3.10 to 3.25 Mg/m , averaging 3.15 Mg/ m .
For mixture proportioning, it may be more useful to express the density as relative density (specific gravity). On an average the specific gravity of cement is 3.15

## Slide 13: Laboratory test of cement
Apparatus;
Le Chaterlier”s flask,
Weighing balance and kerosene (free from water).
Le Chaterlier”s flask, is made of thin glass having a bulb at the bottom. The capacity of the bulb is nearly 250 ml. The bulb is 7.8 cm in mean diameter. The stem is graduated in millimeters. The zero graduation is at a distance of 8.8 cm from the top of the bulb. At 2 cm from the zero, there is another bulb is of length 3.5cm and capacity 17 ml. At 1 cm from bulb, the stem is marked with 18 ml and is grated up to 24 ml. The portion above 24ml mark is in the form of a funnel of diameter 5cm.k

## Slide 14: Procedures;
Laboratory test of cement
 Dry the flask carefully and fill with kerosene or naphtha to a point
on the stem between zero and 1 ml.
 Record the level of the liquid in the flask as initial reading.
 Put a weighted quantity of cement (about 60gm) into the flask so that level of kerosene rise to about 22 ml mark, care being taken to avoid splashing and to see that cement does not adhere to the sides of the above the liquid.
 After putting all the cement to the flask, roll the flask gently in an
inclined position to expel air until no further air bubble rise3s to
the surface of the liquid.
 Note down the new liquid level as final reading.

## Slide 15: Laboratory test of cement
Observation and calculations
 Weight of cement used =W gm
 Initial reading of flask =V1 ml
 Final reading of flask =V2 ml
 Volume of cement particle= V2-V1 ml
 Weight of equal of water= (V2-V1) x specific weight of water.
Specific gravity of cement = (Weight of cement/ Weight of equal volume of water)
= W/(V2-V1)
NOTE:
Duplicate determination of specific gravity should agree within 0.01.
To get more accurate result, the flask should be held in a constant temperature
before each reading is taken.

## Slide 16: Laboratory test of cement
SETTING TIME
Setting refers to a change from liquid state to solid state. Although, during setting cement paste acquires some strength, setting is different from hardening.
 Sinettthinegsttiamnedaisrdtso. determine if a cement sets according to the time limits specified
 Setting time is determined using either the Vicat apparatus or a Gillmore needle .
Vicat Needle
Gil
lmore needle

## Slide 17: SOUNDNESS TEST
between 3-5%
Methods;
 Le-Chatelier method: which determines free CaO
 Autoclave method: which determines both free CaO and MgO
a. Le-Chatelier method
Apparatus;
Soundness is the volume stability of cement paste after setting. The cement paste should not undergoes large changes in volume after it has set.The extra volume change is due to free CaO and MgO. will result in cracking effect.
Note: Magnesium content in cement is limited to 6% and Gypsum content is
Balance, whose permissible variation at a load of 1000g should be +1.0g and Water bath.

## Slide 18: Laboratory test of cement
Procedure:
Place the mould on a glass sheet and fill it with the cement paste formed by gauging cement with 0.78 times the water required to give a paste of standard consistency.
Cover the mould with another piece of glass sheet, place a small weight on this covering glass sheet and immediately submerge the whole assembly in water at a temperature of 27 ± 2oC and keep it there for 24hrs.
Measure the distance separating the indicator points to the nearest 0.5mm (say d1).
Submerge the mould again in water at the temperature prescribed above. Bring the water to boiling point in 25 to 30 minutes and keep it boiling for 3hrs.

## Slide 19: Laboratory test of cement
COMPRESSIVE STRENGTH TEST
Compressive strength is the most important property physical properties of cement. When cement is used for important structures, compressive strength test is always carried out to ascertain quality of cement. Strength test is not made on plain cement due to excess shrinkage and cracking of plain cement paste. Thus the strength of cement is measured using either cement-sand mortar or concrete of prescribe proportions. The British standard method for testing compressive strength of cement BS EN 196-1: 2005 specifies a mortar prism test. The cement-sand mix proportions of 1:3 is adopted with water cement ratio of 0.5, the cubes are 50mm in dimensions.

## Slide 20
Laboratory test of cement
Materials and apparatus used;
 Cement
 Standard sand
 Vibration Machine
 Poking Rod
 Cube Mould of size 70.6 mm X 70.6 mm X 70.6 mm
 Gauging Trowel
 Weigh Balance
 Graduated glass cylinders – 200 to 250 ml capacity

## Slide 21: Laboratory test of cement
Preparation of specimen and test procedures;
 Mixing of material for each test cube shall be separately prepared. The quantities of cement, standard sand and water shall be as follows:
Cement – 200 gms, Standard sand – 600 gms, water – (p/4+3) % of mass (cement +sand)
Where P = % of water required to make cement paste of standard consistency.
All ingredients shall be dry mixed for one minute. After that, water is gradually added till paste is formed of uniform colour. Mixing time shall be between 3-4 minutes. If uniform colour of paste is not achieved after mixing more than 4 minutes, fresh mortar shall be prepared.
 Apply mould oil on interior surface of mould and place the mould on vibrating table. Immediately after preparing mortar as describe in point 2,

## Slide 22: Laboratory test of cement
 Place the mortar Inside cube moulds. Rod 20 times for approximate 8 sec to ensure full compaction of mortar.
 Further compaction shall be done by using vibrating machine. The period of
vibration shall be two minutes at the specified speed of 12 000 ± 400
 After completion of vibration, remove moulds along with base plate and finish the top surface by trowel.
 Keep moulds filled with specimen for 24 ± 1 hr in moist environment. Remove samples from mould and immediately submerge in clean water.
 After curing period is over, remove cubes from water and immediately place in testing machine with side facing upwards. Cubes shall be tested without packing between steel plattens of the testing machine and cubes surface. Load shall be steadily and uniformly applied, starting from zero at a rate of 35 N/mm2/min. till failure of sample.

## Slide 23:  Calculate compressive strength of specimen by
Laboratory test of cement
using following formula compressive strength = P / A where P = Maximum load applied, A = cross-sectional area of test specimen
 Compressive strength shall be calculated as average value of three samples. If value of individual sample is differing more than 10 % of average value, then that value shall not be considered. In that case average of other two samples shall be considered for compressive strength calculation.

## Slide 24: LOSS OF IGNITION TEST
Laboratory test of cement
10 gm of cement is taken on platinum crucible and heated up to a temperature of 900 to 10000C for 15 minutes
The loss due to moisture and carbon dioxide causes weight loss which should not be more than 5% for all cements

## Slide 25: Laboratory test of cement
DAYS | STRENGTH CLASSES |  | 
 | 32.5 | 42.5 | 52.5
2 |  | 10 | 20
7 | 16 |  | 
28 | 32.5 | 42.5 | 52.5